## Slide 1: ME 964: Project -1 Finite Element Formulation for Plates Shiguang Deng Xingchen Liu Goldy Kumar

## Slide 2: FEM for Plates
A plate is a flat three dimensional solid body with
one dimension is much smaller than the other two
zero curvature at mid-surface in the reference configuration
loading that causes bending deformation
membrane and bending response are decoupled
  investigated independently and later superposed
Notes: Do not solve by 3D mesh because: coarse mesh leads to shear locking and ill conditioning, fine mesh end up with too many dof.

## Slide 3: Plate Theories
Kirchhoff plate
extension of the Euler-Bernoulli beam theory
inter element
Prohibit transverse shear
1850s
FE elements are hard to develop
Mindlin plate
extension of Timoshenko beam theory
inter element
Account for transverse shear
1950s
FE elements are easier to develop

## Slide 4: Isoparametric Mindlin Plate FE
Element Stiffness Matrix
Element Type | Selected Integration Rule
 | 9-point
 | 9-point
 | 4-point
Element Type | Selected Integration Rule
 | 9-point
 | 9-point
 | 4-point
Nodal Load Vector

## Slide 5: Heterosis Plate Elements & Gaussian Integration points
x
y
s
t
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
4-point
9-point

## Slide 6: Results:
Plate Analyzed
- A rectangular plate 1x1x.02m3
- All four sides Clamped
- 1 Pa Pressure on the plate
Mid point displacement
From FEM code: 8.69e-9m
From SolidWorks: 8.751e-9m
From Analytical: 8.6e-9m

## Slide 7: Numerical Results & Verification & Challenges
Plate Thickness | FEA(500elems) | Analytical | Errors
2e-2 | 8.687502e-009 | 8.599500e-009 | 1.012976%
1e-2 | 6.893745e-008 | 6.885245e-008 | 0.123287%
2e-3 | 8.629722e-006 | 8.599500e-006 | 0.350209%
1e-3 | 2.485991e-005 | 6.885245e-005 | 63.893921%
Mesh Density | FEA(t=1e-2) | Errors
20 | 2.889219e-008 | 58.037528%
100 | 6.690380e-008 | 2.830182%
500 | 6.893745e-008 | 0.123287%
1000 | 6.922092e-008 | 0.535158%
1500 | 6.914186e-008 | 0.420333%
Analytical | 6.885245e-008 | 0

## Slide 8: Next Step
Based on topology optimization, design of stiffener distributions and orientations for thin plate will be carried out to minimize compliance, stress and buckling stress.

## Slide 9: Next Project- Plate Eigen Value Problem
(General)
Where,
  [M] = ,
  [ C] = , - damping co.
  =
  = + P

## Slide 10: Natural Frequency and Mode Shapes
Undamped and homogeneous EOM
Oscillatory solution:
Solve for Eigen values and Eigen vectors
  Mesh dependent
  Not solved for all values
Use numerical techniques
Vibration mode
A configuration with elastic resistance in balance with inertial loads